Arduino Hacks
Hacking on Arduino
George Patterson
george.patterson@gmail.com
[Speaker Notes: There is only so much that can be covered in approximately two hours and I would rather not talk for that long. Arduino is an open source framework, including the circuit design and construction, firmware and software interface]

---
Summary
Introduction
- Introduction
- Arduino IDE
- Building block theory
- Building block examples
[Speaker Notes: Hello world]

---
Introduction
Introduction
- Started as a platform for art students and general electronic to non-engineers
- Based on an AVR based ATMEL chip
- Based around Open source hardware/software Community grew up around it
- Current version is the Duemillenov or the Duo.
  - Generic off-shoots
    - Freetonics Arduino 2010
    - Various other items
[Speaker Notes: Started as a way to simplifiy embeding a microprocessor into a project for art students and beginners. The arduino is based on an ATMEL AVR processor. Other platform such as PICmicro by Microchip are not that open, see forums regarding the PICKit. Since then it has moved on to become a powerful environment for rapid hardware development. A community has grown around it with contributions to libraries and hardware/firmware improvements. Some off shoots are the Freetronics Arduino 2010 and vairous other boards. They are generally compatible with the official boards.]

---
Basic Theory
Basic Theory
- Electrical
  - Voltage divider
  - Floating Inputs
- Code
  - Arduino program is called a “sketch”
  - Three major components
    1. Editor
    2. Compiler
    3. Serial Terminal
[Speaker Notes: In the way of quick theory, there are a couple of things we need to cover first. Voltage dividers is a linear circuit that produces an output voltage as a ratio of the inut voltage. One trap that is easy to fall into is the floating input. A Binary value can be either 0 or 1. If a input pin is left floating, then it could be either 0, 1 or undetermined where it will be rounded to either 0 or 1. The Arduino IDE contists of an]

---
Voltage Dividers
Voltage dividers
- A voltage divider is a linear circuit that produces a output voltage which is a fraction of the input voltage
- Can be used to step down a larger voltage for montoring purposes.
Image from Wikipedia.org
[Speaker Notes: If you have a 5V rail connected to ground via two equal valued resistors (Z1 and Z2)then the voltage at the junction between the resistors will be 2.5V. If resistor Z1 is 2K Ohms with Z2 resistor being 10K Ohms, what would the voltage be at Vout? 4V Note you could use multiple resitors if you need more than one voltage. I will not be covering this, but the princip is the same. Example 5x 1K Ohms resistors across a 5v rail will give 1V increments They are handy if you are wanting to monitor a voltage and it's above 5V.. such as a car battery voltage (10-15V perhaps). You might want to consider extra components in case someone connects the circuit to a truck or bus (24V). Warranty up in smoke. The negative side of the voltage dvider needs to be connected to the ground of the source that is being monitored.]

---
Arduino IDE
Arduino IDE
- Arduino is a cross-platform development environment for Linux/OS X/Windows
- Three components
  - Editor
  - Compiler
  - Serial Console
- Written in Java
[Speaker Notes: The Arduino IDE is crossplatform for Linux/ OS-X and Windows. It consists of an Editor, Compiler and Serial terminal. Right, on to the “hello world” of Arduino. flashing the in built LED. The langauge is basically C but with the harsh corners removed. For example, Memory Allocation (malloc) isn't necessary, nor desirable. Similarly you do not need for pointers or other hard work. Best approach is to treat the Arduino framework as a macro lanaguage that looks like C. Applying some tricks that you may have learn when C programming could bite your in interesting ways.]

---
Floating Inputs
Floating Digital Inputs
- You have a switch that you wish to connect to your Arduino, How do you do it?
  - Connecting the switch directly to the pin and positive may give the correct result
    - But what happens when you release the button?
    - The switch opens and the input is floating again
  - SPDT – connect one side to positive, other to negative
  - Instead you need to tie the input pin to one of the rails and then connect the input pin to the other rail via the switch.
[Speaker Notes: Question: What happens when you release the switch? Answer; The switch opens and the input is floating again. (White board??) A beginners trick is to create use a Double Throw switch and connect one side to positive and the other side to the ground rail.. The better option is tho tie the input pit either high (positive) or low (ground).]

---
Blinken Liten (start)
Blinken Liten
Two main functions: setup() and loop()
void setup() {
}
void loop() {
}
[Speaker Notes: On Pin 13 of the Arduino is a surface mounted LED which can be used for helping to debug a arduino program. The Pin 13 LED already as the current limiting resistor fitted so you don't need anything more to use it. Better, you can plug a LED between pin 13 and ground if you can't see the surface mount LED. There are two major functions, setup( and main(). The code in the void setup() is executed only once, while the loop section will run endlessly to the end of time. Well, 23.5 days if you are using millis() timers.]

---
Blinken Liten (setup)
Blinken Liten (setup)
Two main functions: setup() and main()
void setup() {
 // initialize the digital pin as an output:
 pinMode(13, OUTPUT);
}
void loop() {
}
[Speaker Notes: Into the setup() function we initialise pin 13 to be an output pin.]

---
Blink Liten (main part 1)
Blinken Liten (main part 1)
Two main functions: setup() and main()
void setup() {
 // initialize the digital pin as an output:
 pinMode(13, OUTPUT);
}
void loop() {
 digitalWrite(13, HIGH); // set the LED on
 delay(1000); // wait for a second
}
[Speaker Notes: In loop() we set pin 13 to HIGH and then delay execution for 1000 milliseconds. The delay routine is similar to the sleep command in Unix. Note much more to. Now we need to turn the LED off and wait another 1000milliseconds.]

---
Blinken Liten (main part 2)
Blinken Liten (main part 2)
Two main functions: setup() and main()
void setup() {
 // initialize the digital pin as an output:
 pinMode(13, OUTPUT);
}
void loop() {
 digitalWrite(13, HIGH); // set the LED on
 delay(1000); // wait for a second
 digitalWrite(13, LOW); // set the LED off
 delay(1000); // wait for a second
}
[Speaker Notes: Right, this code is the same but instead of setting the pin to High, we set the pin to Low. Again a delay routine will cause the microprocessor to pause for a period of time. And that's Hello World.. easy wasn't it!]

---
Blinken Liten (Review)
Blinken Liten (Review)
- It's good but not great.
  - Supposing you wanted to control the device via another pin or you needed pin 13 for something else
- The solution is to define a constant instead of hard coding.
- “Fix it in software”
[Speaker Notes: The problem with the preceeding code is that the pin has been hard coded and requires multple changes if you need to change the hardware. As an example some pins are connected to the serial port. Some other pins are used for I-squared-C (i2c) which is required if you wish to monitor temperature sensors. What you want to try to aviod is having to hack a software solution for something that would have been similar if you had been a little be more careful with pin assignment.]

---
Blink Liten (contants)
Blinken Liten (Constants)
Define a constant such as ledPin
#define ledPin 13; // the number of the LED pin
void setup() {
 // initialize the digital pin as an output:
 pinMode(ledPin, OUTPUT);
}
void loop() {
 digitalWrite(ledPin, HIGH); // set the LED on
 delay(1000); // wait for a second
 digitalWrite(ledPin, LOW); // set the LED off
 delay(1000); // wait for a second
}
[Speaker Notes: At the top of you program add the line const int ledPin = 13. This will declare a constant of ledPin to be a integer with the value of 13. Afterwards, replace the number 13 in the digitalWrite with ledPin. Finally recompile and upload the sketch to the Arduino.]

---
Digital Input and Serial
- Serial Port
  - Arduino provides a serial port to assist with debugging
    - Start the serial port with Serial.begin(<speed>)
    - Send some data with Serial.print() or println()
    - Receive data with Serial.read()
  - To read a digital input, use digitalread(<pin no>)
[Speaker Notes: The serial port can be invaluable for testing as you can “print” multiple debug statements to figure out where you code is going wrong.]

---
Digital Input and Serial (cont'd)
- Most of this is the same as before.
  - Initialise the serial port, and set pin 2 as an Input.
  - In loop(), read the input pin and write the value to the serial port
  Void setup() {
   Serial.begin(9600);
   pinMode(2, INPUT);
  }
  void loop() {
   int sensorValue = digitalRead(2);
   Serial.println(sensorValue, DEC);
  }
[Speaker Notes: We have seen this before. In void setup() we are setting the Arduino serial port to 9600 baud and the pin mode of pin two to be an input pin. In void loop(), the Arduino will read the value of pin2 and print the data as a decimal number. For real project, you'd need to debounce the contacts. The contacts on almost any sort of switch or push button will bounce when they close and possibly when they close. Thatt is if you are watching for a button being pressed, the Arduino will receive multiple pulses which will trigger your code if you haven't taken precautions.]

---
Analogue Read
analogRead(analogPin) is new here.
int analogPin = 3;
int val = 0; // variable to store the value read
void setup()
{
 Serial.begin(9600); // setup serial
}
void loop()
{
 val = analogRead(analogPin); // read the input pin
 Serial.println(val); // debug value
}
[Speaker Notes: The AnalogRead will read the voltage that is applied to analogPin and convert it into a 10 bit number. Note: The Analog port is only appropriate for low voltages. If you are interested in monitoring higher voltages, consider either a voltage divider or a more complex circuit. Be aware of high voltages!]

---
Floating Analog Inputs
Floating Analog Inputs
- You wanting to read a potentiometer
- Connect one of the outer pins to ground, the other to your 5v rail. The middle pin (wiper) is connected to an alogue pin (ADC).
  - What's the design pattern being used?
  - The switch opens and the input is floating again
[Speaker Notes: Question: What happens when you release the switch? Answer; The switch opens and the input is floating again. (White board??) A beginners trick is to create use a Double Throw switch and connect one side to positive and the other side to the ground rail.. The better option is tho tie the input pit either high (positive) or low (ground)]

---
Floating Analog Inputs (cont'd)
Floating Analog Inputs (cont'd)
- There is a catch though...
- Arduino has a 10-bit number but can be a electrically noisy (Actual +/-5mV). Each step in value represents between 0.005V.
- Solution: Only process a large change or right shift the number by one bit. (Faster than dividing by 2)
[Speaker Notes: Question: What happens when you release the switch? Answer; The switch opens and the input is floating again. (White board??) A beginners trick is to create use a Double Throw switch and connect one side to positive and the other side to the ground rail.. The better option is tho tie the input pit either high (positive) or low (ground)]

---
Interprocessor Comms
Interprocessor Communications
- CAN Bus – originally Car Area Networking
  - Patent filled minefield if going semi-commercial
- I2C Inter communications
  - Works okay for short runs, Arduino has enough smarts to do this natively when requested.
- RS-485 – Long distance Multidrop serial
  - Master/Slave configuration for up to 32/64 nodes
    - Use SN65176B or similar.
- Many others
[Speaker Notes: If you find that you are running out of Pins on the Arduino or you need to distrubte the I/O load for whatever reason, you may need to consider using more than one Microcontroller. The solutions could be CAN bus, used in multiple places including cars and rockets. I2C is a simple protocol if the bus length is fairly short. RS-485 – Multidrop serial for up to 32 or 64 nodes (depending on the chip used). It's also is immune to noise by having a inverted signal on a separate wire. You may have have the option of using multipexing or a Dedicated IC such as a MAX72219 or 21 There are plenty of other communications protocols and bus scheme. I would suggest experimenting with a scheme that had been documented by someone else first.]

---
Reference Books
Reference Books
- Getting Started with Arduino
  - Written by Massimo Banzi
- Practial Arduino
  - Written by Jonathan Oxer and Hugh Blemmings
- Any others??
[Speaker Notes: While the web is good, it is always nice to have the option of being able to pick up a book and step away from the computer for a bit. Two books that I have read are Getting Started with Arduino and Practical Arduino. Taking the first one first, I found that Getting Started with Arduino assume that you have no electronic knowledge and takes a while to get going with a circuit or code. I guess it has been wriiten to “teach designers the bare minimum of elctronics so they can build interactive prototypes” so itwill be slow starting and doesn't really ramp up in a technical way. Practical Arduino will launch you head first into the environment. Unfortunately the layout left a bit to be desired, in my opinion. Please don't blame the authors for that one!]

---
Closing remarks
- Explore the Arduino Playground:
  - http://www.arduino.cc/playground/
- Join a hackerspace :-)
  - http://www.hackmelbourne.org
- Read the data sheet!
- Any questions??
[Speaker Notes: While I will not carry on, I will say that embedded programming can be confusing as to what is happening inside the tiny black box. The best advice is to go back to an earlier version of the code and work forward to what doesn't work. Another way to solve the problem is to create a stub for the section that you are struggling on. Most of all don't waste days getting annoyed; please ask around! Local hacker spaces are a good resource. Otherwise anyone who has a logical mind might be able to pick you typing error.]